NAME:MEGHANA GANESH
REG NO:210905160
CSE A

LAB EXERCISES

Configure two VMs that will be used to test connectivity from end to end and R1 will
serve as a DHCP server to distribute IP addresses. The diagram below details the
current setup:

1. In order to configure our router as a DHCP server the following commands were used.
R1(config)#IP dhcp pool NAME
R1(dhcp-config)#Network 192.168.3.0 255.255.255.0
R1(dhcp-config)#Default-router 192.168.3.1
The commands above create a DHCP pool, adds the network that we want to assign IP addresses
from, and specifies the default gateway for this subnet.
Note: There are many other parameters that go into configuring a DHCP server but this will
suffice for our test environment.
That should be it for the DHCP configuration.

2.The next thing that you want to do is configure the fastethernet 0/0 interface which will
connect to our switch.
R1(config)#Interface fastEthernet 0/0
R1(config-if)#No shutdown
R1(config-if)#ip address 192.168.3.1 255.255.255.0

The commands above will turn the interface on and assign an IP address.
3. Turn on the VPCS. In PC1 and PC2 type dhcp
PC1>dhcp
PC2>dhcp

4. Let’s analyze some of the traffic patterns using Wireshark.
In Wireshark we see the following information with regards to DHCP:

2. Network Prefixes and Routing
In this exercise, you study how the network prefixes (netmasks) play a role when hosts determineif a datagram can be
directly delivered or if it must be sent to a router.
This part uses the network setup shown in Figure 8.2. The network includes one router, four
hosts and two hubs. The IP addresses of all devices are given in Table 8.1. Here, each host hasonly a
default route. In other words, the routing table at a host only knows about the directly connected networks and the default gateway.

R1(config)#ip dhcp pool subnetwork1
R1(dhcp-config)#network 10.0.1.0 255.255.255.0
R1(dhcp-config)#default-router 10.0.1.1
R1(dhcp-config)#exit
R1(config)#ip dhcp pool subnetwork2
R1(dhcp-config)#network 10.0.2.0 255.255.255.0
R1(dhcp-config)#default-router 10.0.2.138
R1(dhcp-config)#exit

R1(config)#inter f0/0
R1(config-if)#no shutdown
R1(config-if)#ip address 10.0.1.1 255.255.255.0
R1(config-if)#exit
R1(config)#inter f0/1
R1(config-if)#no shutdown
R1(config-if)#ip address 10.0.2.138 255.255.255.0
R1(config-if)#exit
R1(config)#do wr

PC1> dhcp
DDORA IP 10.0.2.1/24 GW 10.0.2.138

PC2> dhcp
DDORA IP 10.0.2.3/24 GW 10.0.2.138

PC3> dhcp
DDORA IP 10.0.2.2/24 GW 10.0.2.138

PC4> dhcp
DDORA IP 10.0.1.2/24 GW 10.0.1.1

CLASSWORK QUESTION:

R3:
R3#conf t
R3(config)#ip dhcp pool nwlab
R3(dhcp-config)#network 191.168.1.0 255.255.255.0
R3(dhcp-config)#default-router 191.168.1.254
R3(dhcp-config)#ip dhcp pool oslab
R3(dhcp-config)#network 172.16.59.0 255.255.255.0
R3(dhcp-config)#default-router 172.16.59.254

R3(config)#inter f0/0
R3(config-if)#ip address 20.0.0.2 255.255.255.0
R3(config-if)#no shutdown
R3(config-if)#exit

R3(config)#ip route 191.168.1.0 255.255.255.0 20.0.0.1
R3(config)#ip route 172.16.59.0 255.255.255.0 20.0.0.1
R2:
R2#conf t
R2(config)#inter f0/0
R2(config-if)#ip address 20.0.0.1 255.255.255.0
R2(config-if)#ip helper-address 20.0.0.2
R2(config-if)#no shutdown

R2(config-if)#exit

R2(config)#ip route 20.0.0.0

R2(config)#ip route 20.0.0.0 255.255.255.0 20.0.0.2
R2(config)#ip route 191.168.1.0 255.255.255.0 10.0.0.1
R2(config)#ip route 172.16.59.0 255.255.255.0 10.0.0.1

R1:
R1#conf t
R1(config)#inter s1/0
R1(config-if)#ip address 10.0.0.1 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#ip helper-address 20.0.0.2
R1(config-if)#exit

R1(config)#inter f0/0
R1(config-if)#ip address 191.168.1.254 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#ip helper-address 20.0.0.2
R1(config-if)#exit

R1(config)#inter f0/1
R1(config-if)#ip address 172.16.59.254 255.255.255.0
R1(config-if)#no shutdown
R1(config-if)#ip helper-address 20.0.0.2
R1(config-if)#exit

R1(config)#ip route 20.0.0.0 255.255.255.0 10.0.0.2
R1(config)#do wr